## Slide 1: An Introduction to the Multichannel Rendezvous Problem
Prof. Cheng-Shang Chang (張正尚教授)
Institute of Communications Engineering National Tsing Hua University
July 2025

## Slide 2: Joint works with Prof. Wanjiun Liao, Prof. Duan-Shin Lee, Prof. Jang-Ping Sheu, and their students
Cheng-Shang Chang, Wanjiun Liao and Ching-Min Lien, "On the multichannel rendezvous problem: fundamental limits, optimal hopping sequences, and bounded time-to-rendezvous,“ Mathematics of Operations Research, vol. 40, no. 1, pp. 1-23, 2015
Cheng-Shang Chang, Wanjiun Liao, and Tsung-Ying Wu, "Tight lower bounds for channel hopping schemes in cognitive radio networks," IEEE/ACM Transactions on Networking, vol. 24, no. 4, pp. 2343-2356, 2016.
Cheng-Shang Chang, Cheng-Yu Chen, Duan-Shin Lee, and Wanjiun Liao, "Efficient encoding of user IDs for nearly optimal expected time-to-rendezvous in heterogeneous cognitive radio networks," IEEE/ACM Transactions on Networking, vol. 25, no. 6, pp. 3323-3337, 2017.
Yeh-Cheng Chang, Cheng-Shang Chang, and Jang-Ping Sheu, "An enhanced fast multi-radio rendezvous algorithm in heterogeneous cognitive radio networks," IEEE Transactions on Cognitive Communications and Networking, vol. 4, no. 4 pp. 847-859, 2018.
Cheng-Shang Chang, Jang-Ping Sheu, and Yi-Jheng Lin,"On the theoretical gap of channel hopping sequences with maximum rendezvous diversity in the multichannel rendezvous problem," IEEE/ACM Transactions on Networking, vol. 29, no. 4, pp. 1620--1633, Aug. 2021.
Guann-Yng Jiang and Cheng-Shang Chang, "Locality-sensitive hashing for efficient rendezvous search: A new approach,'' IEEE Transactions on Communications, vol. 72, no. 9, pp. 5674--5687, Sept. 2024.

## Slide 3: Outline
Multichannel rendezvous problem in cognitive radio networks
Problem formulation and classification
Asymmetric setting
Symmetric setting with time synchronization
Symmetric setting without time synchronization
Oblivious rendezvous
Summary

## Slide 4: Multichannel Rendezvous Problem in a CRN
In cognitive radio network (CRN), the secondary users (SUs) could use the unused licensed spectrum without interfering the neighbor primary users (PUs).
Notes: In a cognitive radio network, the secondary users can only use the channels which are not used by the primary users.
For example,
There are three channels, PU1 use channel 0 and PU2 use channel 1.
So the available channel of SU1 is 2. The available channels of SU2 are 0 and 1.
In addition, the available channel sets of SUs are changed with time.
The available channel sets of the SUs vary from time and their locations.

## Slide 5: Multichannel Rendezvous Problem in a CRN
Before transmitting data, the two neighboring SUs should find a common available channel as the control channel (pair-wise control channel) for exchanging control messages.
However, establishing the control channel is a challenging problem because the SUs may not know which channels are available for their neighbors.
sender
?
receiver
(common available channel)
control channel
Notes: When the SU wants to send data to its destination, they must find a common available channel as the control channel for exchanging the control messages.
However, the SU can not know which channels are available for its destination.
Setup the control channel in cognitive radio networks is a challenge.

## Slide 6: Rendezvous search problem
Alpern (1973): The rendezvous search problem asks how two unit speed searchers, randomly placed in a known search region Q, can minimize the time required to meet.
Anderson and Weber (1990): Rendezvous problem on discrete locations

## Slide 7: Multichannel rendezvous problem

## Slide 8: Multichannel Rendezvous Problem
Rendezvous problem on labeled channels
Two users
N channels
Designated control channel:
  Control channel overload
  Jamming attack
  Control channel may not be available to a user
Users hop through the N channels to meet.

## Slide 9: Problem classification of rendezvous search problem
User: asymmetric strategy (easy) vs. symmetric strategy(hard)
Time: synchronous clock (easy) vs. asynchronous clock (hard)
Space:
  Labelled channels vs. unlabeled channels
  homogeneous vs. heterogeneous (available channel set)

## Slide 10: Classification the MRP problems

## Slide 11: Classification the MRP problems
users/time/channels/labels representation for an MRP problem
sym/sync/homo/global

## Slide 12: Problem formulation of the multichannel rendezvous problem
A system with N labelled channels, indexed from 0,1,…,N-1.
The discrete-time setting, t=0,1,2,…
The available channel set for user i,
where is the number of available channels to user i.
Assume that there is at least one channel that is commonly available to the two users

## Slide 13: Problem formulation of the multichannel rendezvous problem
Two users: X1(t) (resp. X2(t)) is the channel selected by user 1 (resp. user 2) from its available channel set at time t.
The time-to-rendezvous (TTR), denoted by T, is the number of time slots (steps) needed for these two users to select a common available channel, i.e.,
MTTR: Maximum TTR (worst-case)
ETTR: Expected TTR (average-case)

## Slide 14: Asymmetric Setting: Homogeneous available channel sets
The ``wait-for-mommy'' strategy
User 1 plays the role of ``mommy'' who uniformly selects at random a channel to start and then cycles through the N channels.
User 2 plays the role of ``child'' who also uniformly selects at random a channel and stays there until it is found by the ``mommy.''

## Slide 15: The Classical Wait-for-mommy Strategy (Anderson and Weber (1990))
Consider a two-user rendezvous problem with N unlabeled locations
The mommy goes through each location sequentially, while the child stays at the same location. They rendezvous within N steps (optimal in MTTR)

## Slide 16: The asym/async/hetero/local MRP
Using the ``wait-for-mommy'' strategy is a little bit tricky as the ``child'' does not know how long it has to stay on the same channel.
If it stays on a channel that is not in the available channel set of the ``mommy,'' then it will not be found.
The solution is for the two users to cycle through their available channels like the ``mommy'' in the ``wait-for-mommy'' strategy, but do so with coprime periods.

## Slide 17: Chinese Remainder Theorem
It was first discovered in the 3rd century AD by the Chinese mathematician Sunzi in Sunzi Suanjing (孫子算經).
if n1 and n2 are coprime, and r1 and r2 are nonnegative integers such that ri <ni, then there is one and only one nonnegative integer x, such that x < n1n2 and

## Slide 18: Chinese Remainder Theorem
“今有物不知其數，三三數之賸二，五五數之賸三，七七數之賸二，問物幾何？”
三人同行七十希，五樹梅花廿一支，七子團圓正半月，除百零五便得知

## Slide 19: Chinese Remainder Theorem
If n1 and n2 are coprime, and user i can simply cycle through its available channel set repeatedly and every pair of available channels for user 1 and 2 will appear exactly once in a period of n1n2 time slots.
If n1 and n2 are coprime, then rendezvous is guaranteed within n1n2 time slots.
But how can we be sure that n1 and n2 are coprime?

## Slide 20: The modular clock algorithm

## Slide 21: An example of the CH sequences of the modular clock algorithm
To make sure that the selected periods p1 and p2 are coprime, user 1 selects an odd number that is not smaller than n1 and user 2 selects a power of 2 that is not smaller than n2
c1={1,2,3,4}, p1=5.
c2={2,5}, p2=2.

## Slide 22: The sym/sync/homo/global MRP
A Galois field GF(N) is a set of N elements with two operations ``addition’’ and ``multiplication’’ that satisfy various algebraic properties, including the associative law, the commutative law and the distributive law.
Intuitively, we can add, subtract, multiply and divide in a Galois field as in rational numbers.
When N is a prime, the addition is the usual addition with the modulo N operation, and the multiplication is the usual multiplication with the modulo N operation.

## Slide 23: The synchronous modular clock algorithm (in a Galois field)

## Slide 24: The synchronous modular clock algorithm (in a Galois field)
If both users generate their CH sequences by using the synchronous modular clock algorithm, then the two users will rendezvous within N+1 time slots (optimal in MTTR).
For t=1,2,…,N, the CH sequence is simply a "line" in the field GF(N) with the slope r and the bias b.
If these two users select the same slopes, they rendezvous at time 0.
If these two users select different slopes, then these two lines intersect each other within [1,N+1].

## Slide 25: An example of the CH sequences of the synchronous modular clock algorithm
N=5 and there are five channels {0,1,2,3,4}.
User 1 (resp. user 2) chooses r1=1 and b1=0 (resp. r2=2 and b2=0).